## Slide 1: UNIT 1: General Physical and Biological concepts- Mass, Density, range of electromagnetic radiation, interaction between matter and radiation, fluorescence, phosphorescence. pH and buffers. Significance of instrumentation in Forensic Science. Centrifuge- Principles, types and Forensic applications

## Slide 2
Mass: Mass is the quantity of matter in a substance. S. I UNIT: KG
Density: The density, of a substance is its mass per unit volume. The symbol most often used for density is ρ, density is defined as mass divided by volume. S I UNIT: KG/M3
Interaction between matter and radiation
The term radiation applies to the emission and propagation of energy through space or a material.
No mass or physical form.
Travel at speed of light ( c ) in a vacuum (or air)
Unaffected by electric or magnetic fields and gravity
In Passing through the matter, the intensity is reduced, because of absorption & scattering .
Radiation intensity is inversely proportional to the square of the distance from the source at any place

## Slide 3: Range of electromagnetic radiation

## Slide 4
Electromagnetic spectrum
The EM spectrum is generally divided into seven regions, in order of decreasing wavelength and increasing energy and frequency. The common designations are: radio waves, microwaves, infrared (IR), visible light, ultraviolet (UV), X-rays and gamma rays.
The electromagnetic spectrum includes, from longest wavelength to shortest: radio waves, microwaves, infrared, optical, ultraviolet, X-rays, and gamma-rays.
Which lists the waves in order of frequency from highest to lowest?
The correct order of waves in the descending order of frequency is - Visible light,infrared ,micro wave.
As per electromagnetic spectrum, the gamma wave has the maximum frequency and radio wave has the least frequency. Gamma rays > X- ray > U.V ray > Visible light > Infrared wave > Micro wave > Radio wave.

## Slide 5
Fluorescence
Fluorescence is the emission of light by a substance that has absorbed light or other electromagnetic radiation. It is a form of luminescence. In most cases, the emitted light has a longer wavelength, and therefore a lower photon energy, than the absorbed radiation.
Phosphorescence
Phosphorescence is a type of photoluminescence related to fluorescence. When exposed to light of a shorter wavelength, a phosphorescent substance will glow, absorbing the light and reemitting it at a longer wavelength. Unlike fluorescence, a phosphorescent material does not immediately reemit the radiation it absorbs.
Both fluorescence and phosphorescence are based on the ability of a substance to absorb light and emit light of a longer wavelength and therefore lower energy.
Emission of photons from electronically excited states is known as luminescence.

## Slide 6
pH and buffers
pH is a measure of the concentration of H+ [H3O+] ions in a solution. Only the concentration of H+ and OH- molecules determine the pH. When the concentration of H+ and OH- ions are equal, the solution is said to be neutral. If there are more H+ than OH- molecules the solution is acidic, and if there are more OH- than H+ molecules, the solution is basic.
The pH in cells (6.8) and the blood (7.4) are both very close to neutral, whereas the environment in the stomach is highly acidic, with a pH of 1 to 2.
The pH scale measures the concentration of hydrogen ions (H+) in a solution.
An acid is a substance that increases the concentration of hydrogen ions (H+) in a solution, usually by dissociating one of its hydrogen atoms. A base provides either hydroxide ions (OH–) or other negatively-charged ions that react with hydrogen ions in solution, thereby reducing the concentration of H+ and raising the pH.
BUFFER
Buffers usually consist of a weak acid and its conjugate base(basically an acid that loses its hydrogen ion); this enables them to readily absorb excess H+ or OH–, keeping the system’s pH within a narrow range.
To be able to add a strong acid or base to a solution without causing a large change in the pH, we need to create a buffer solution.
Maintaining a constant blood pH is critical to a person’s well-being. The buffer that maintains the pH of human blood involves carbonic acid (H2CO3), bicarbonate ion (HCO3–), and carbon dioxide (CO2),
Antacids, which combat excess stomach acid, are another example of buffers.

## Slide 7
Significance of instrumentation
The use of various instrumental techniques has become an important part of chemical analysis in various fields of science i.e. pure and applied science.
Only a single instrument cannot solve an analytical issue, instead numerous instrumental methods are necessary for efficient analysis to a maximum extent.
A physical property of the sample to be analysed is chosen in instrumental analysis for determination of its chemical composition.
Analysis of the sample can be of any type i.e. biochemical, organic, inorganic, physical or analytical.
Irrespective of the type of analysis, the main purpose to be served is to extract information about the composition of the sample. This is the reason why instrumental analysis is also known as quantitative analysis. The type of instrumental technique used depends on the property of the sample measured.
The basic principle of an instrument employed for chemical analysis is that it can convert chemical information retrieved from the sample to a form which can be easily observed and understood. The instrument chosen for analysis thus helps in:
 Generation of a signal
 Transformation of a signal to one of a different nature (transducer)
 Amplification of the signal.

## Slide 8
Limitations of Instrumental Analysis
There are various limitations of Instrumental analysis as well. These are:
The precision and sensitivity depend on the instrument and will vary accordingly.
The cost of the equipment is quite high. ·
The range of concentration that would be measured is limited. ·
Handling of every instrument is suggested only after training.
Appropriate space is needed.
There must be no fluctuation in the power supply

## Slide 9: Centrifuge- Principles, types and Forensic applications
Centrifugation is a method of separating molecules having different densities by spinning them in solution an axis(centrifuge rotor)at high speed.
Centrifuge is a machine with rapidly rotating container that applies centrifugal force to its contents, typically to separate fluids of different densities or liquids from solids .
Centrifugal force: the apparent force that acts outwardly away from the center of rotation.
Basically, all centrifuge instruments consist of a motor which spins a rotor holding the experimental sample. It is predominantly used to segregate particles or macromolecules like cells, sub-cellular components like nucleic acids and proteins on the basis of their sedimentation rate. The sample gets separated due to variation in their sedimentation rate because of their different shape, size, viscosity of the medium, density, and the rotational speed of the rotor to separate
In 1925, Theodor Svedberg designed the first Analytical Ultracentrifuge.

## Slide 10: principle
The centrifuge encompasses principle of sedimentation, where the acceleration at centripetal force reasons denser constituents to isolate out beside the radiating direction at the bottom most of the tube. With the similar theory lighter substances will be likely to move to the top of the tube. Particle with more density than the solvent residue and the particle with lesser density than, it drift the solution to the top.
The greater the difference in density, the faster they move. In Isopycnic conditions, i.e., where there is no difference in density, the particles remains stable. To take benefit of even minute differences in density to separate different particles in a solution, gravity can be substituted with the much more potent “centrifugal force” delivered by a separator.
According to the Sedimentation Theory, sedimentation is the affinity of particles in suspension to settle down in the fluid where they are pulled and come to rest against a barrier. This is on account of their motion through the fluid in response to the forces acting on them. These forces are due to of gravity, centrifugal speeding up or electromagnetism.
The value for a molecular sedimentation velocity in a centrifugal field is called as its Svedberg constant or S.
FORENSIC APPLICATIONS
Centrifuges are widely used in the field of forensic biology & serology and forensic chemistry. the technique is employed to isolate and determine specific analytes in samples of blood, urine, poisons, toxins, DNA and other compounds for trace analysis, drug analysis, DNA profiling, elemental analysis, analysis of unknown chemicals, toxin and heavy metal evaluation, fingerprinting identification, and compound determination.

## Slide 11: Types of centrifuges
Broadly, Centrifuges are classified into two categories:
Laboratory Centrifugation
Preparative Centrifugation
Laboratory Centrifugation: Laboratory centrifuges are used for small-scale separation and clarification. Characteristic liquid capacities controlled by such devices are in the range of 1 - 5000 ml. The solid to be centrifuged is dispersed into suitable numbers of centrifuge tubes (that appears as test tubes) which is joined in a symmetric method to a revolving block known as the rotor. There are two kinds of rotors i.e., fixed angle rotors and swing out rotors. The fixed angle rotor grips the centrifuge in an immovable way at specific angle to the axis of rotation whereas swing out rotors clamp the tubes analogous to the axis of rotation though the rotor is immobile but when the rotor comes in motion, the tubes blow out in a way that they are aligned perpendicular to the axis of rotation.
Preparative Centrifugation: Preparative centrifuges can handle considerably more liquid capacities as compare to the laboratory centrifuges, which characteristically fluctuating from unit liter to some thousand litres. Its various types are discussed further.

## Slide 12
Types of Centrifuges Used in Laboratories and Their Uses
A centrifuge is a piece of equipment that puts an object in rotation (spins it in a circle) around a fixed axis. This is done by applying a force perpendicular to the axis of the spin. This force can be extremely strong.
While different types of centrifuges exist, they all work on the same sedimentation principle.
How Do Different Types of Centrifuges Work?
In laboratories, centrifuges are used for separating two materials that have similar densities, or when insoluble particulates exist in a dissolved solution.
As mentioned, all types of centrifuges work on the sedimentation principle, where the acceleration of the rotor causes a centripetal force to act upon the rotor and centrifuge tubes. Due to this action, the denser substances in the tubes are forced to outward in a circular direction, while the lighter particles move towards the center.
Sometimes, several particles stick to the bottom of the centrifuge tubes. These particles are called pellets, and the clear solution is known as the supernatant.
Typically, a centrifuge is set to spin at a certain number of revolutions per minute (rpm) or rotational speed. However, two rotors can have the same rotational speed despite different diameters. The acceleration of such rotors will differ too due to the differing radii and angular momentums.
The size of the rotor also has an impact. This is why, Relative Centrifugal Force (RCF) is the accepted standard unit.

## Slide 13
1. Microcentrifuge
As the name suggests, these are extremely compact in design and, therefore, have a smaller footprint that takes up little space on the workbench.
These are apt for use with small tubes (up to 2.0 ml) and often find use in biological applications.
Some of these come with a different rotor or rotor adaptors that can accommodate tubes of various sizes.
These are used for holding pelleting nucleic acids, and for pelleting proteins from solutions as well as microfiltration of minor aqueous samples
2. Refrigerated Centrifuges
These are used for samples that need to be stored at a consistent temperature. It is important that these centrifuges function at maximum speeds while maintaining a steady temperature.
The temperature range of refrigerated centrifuges is between -20 and -40 degrees Celsius, which makes them perfect for analyzing DNA, RNA, PCR, and antibodies.
The compartments of refrigerated centrifuges are sealed as needed by the material.
They can be found in varying configurations such as the swing bucket, fixed angle or both.
Small and large capacity refrigerated centrifuges have different uses.
They are typically used for gathering materials that sediment swiftly such as yeast cells, chloroplast, and more.

## Slide 14
3. High-Speed Refrigerated Centrifuges
Among the different types of centrifuges, these ones can produce substantial force for gathering cellular debris, micro-organisms, larger cell organelles, and proteins.
High-speed refrigerated centrifuges come in an array of sizes and holding capacities.
4. Ultracentrifuges
These centrifuges can generate acceleration of up to 1,000,000 g, which is extremely high.
With ultracentrifuges, users can take advantage of the tiny differences between molecules such as proteins and nucleic acids for the separation
Preparative ultracentrifuges are employed to purify macromolecules such as proteins and nucleic acids based on their physical properties such as size, molecular weight, density and mobility. The high rotating speeds used in ultracentrifuges can generate substantial amount of heat requiring cooling measures to be attached with these devices.

## Slide 15
There are two types of ultracentrifuges:
a. Preparative Ultracentrifuges
These are most commonly used to separate particles on the basis of their densities, isolation of denser particles for pellet collection as well as clarifying suspensions that contain particles.
They help isolate macromolecules and lipoprotein elements from plasma as well as perform de-protonisation of physiological fluids for studying amino acids.
A preparative ultracentrifuge can be furnished with different types of rotors that spin numerous samples at different angles and speeds.
b. Analytical Ultracentrifuges
These come with a light-based optical detection system, which enables real-time monitoring of samples as they spin.
Users can actually see the sedimentation process. They can look at the sample as it concentrates with increasing centrifugal force.
Some of the optical systems used for analysis include the light absorption system, the alternative Schlieren system, and the Rayleigh interferometric system.